## Slide 1
Deep Hole Drilling

## Slide 2: What is a “Deep Hole”?
Any hole more than 5 diameters deep is a Deep Hole
Deep Holes are hard because:
  Chip Clearing
  Lubrication & Cooling
  Tolerances: Position, Diameter, Straightness, & Finish

## Slide 3: Deep Hole Techniques
> 20 Diameters
Gun Drills &
Other Exotica
Limit: ~400
Diameters
5 - 7 xD
Peck
Drill
7 - 10 x D
Parabolic
Flutes +
Peck
< 5 Diameters
No worries!
> 10 x Diameters
Parabolic + Custom Drill Cycles

## Slide 4: Peck Drilling Strategies: > 5 Diameters
Above 5 diameters, start peck drilling
Short pecks up to 10 Diameters
Long Retract > 10 Diameters
Don’t retract clear of holes
Don’t peck carbide drills

## Slide 5: Parabolic Drills: > 7 Diameters
Geometry altered for better chip extraction
Better Feeds & Speeds
Deeper Holes

## Slide 6: Custom Drill Cycles: > 10 Diameters
First Peck: 3 x D
Chip Break: 3 – 10 x D
Full Retract: > 10 x D
Peck Distance Reduces Each Peck
Tip Never Leaves Hole

## Slide 7: What’s To Do After 20 Diameters?
Gun Drills & Similar Approaches
Through tool high pressure coolant
Lots of chip clearance
Requires no reaming or honing
Up to 400x diameters deep!

## Slide 8
Deep Hole Drilling
Thanks!